MATERIAL SAFETY DATA SHEET

Section 1: PRODUCT AND COMPANY IDENTIFICATION   					Rev. Date: 2/5/09		Page 1 of  3

Product Name: Sunny Wax

Product Use: Automotive Detailing

Manufactured for:

Section 2: Hazard(s) Identification

Route of Entry:		See Below

Target Organs:		No Information

Inhalation:		Inhalation irritant. Use in open or well ventilated areas.

Skin Contact:		May Cause mild irritation.

Eye Contact:		May cause irritation.

Ingestion:		Harmful if swallowed.

Health: 1		Flammability: 2			Reactivity: 0

Section 3: Composition of Ingredients

CAS# / EC#			Percent		Chemical Name

8052-41-3 /			5 – 15%		Mineral Spirits

63148-62-9 /			1 – 10%		Siloxanes and Silicones

Mixture				15 – 20%	Proprietor wax mixture

Section 4: FIRST AID MEASURES

Inhalation: 	If breathing is difficult or irritating, move to fresh air immediately. If symptoms persist, get medical attention.

Skin Contact:	Rinse area with soap and water. Seek medical attention if any redness or irritation persists.

Eye Contact:	Flush immediately with large amounts of clean water for a minimum of 15 minutes, lifting upper and lower lids occasionally

Do not rub eyes. If any irritation persists, seek medical attention.

Ingestion:	If swallowed, do not induce vomiting: seek medical advice immediately and show the container or label of product ingested.

Section 5: FIRE FIGHTING MEASURES

Flash Point: 			>180F

Flash Point Method: 		Closed Cup

Extinguishing Media: 		Regular Foam, Carbon Dioxide, Water fog, or Dry Chemical

Hazardous Decompositions: 	None

Special Fire Fighting Procedures: 	N/A

Unusual Fire/ Explosion Hazards: 	N/A

Flammability Classification:	Combustible Liquid (U.S. Domestic) / Non-Flammable (EU International)

MATERIAL SAFETY DATA SHEET

Sunny Wax

Section 6: ACCIDENTAL RELEASE MEASURES						Rev. Date 2/5/09		Page 2 of  3

Contain large spills with dikes to prevent entry to waterways and sanitary sewers and transfer the material to appropriate containers for reclamation or disposal. Absorb/trap remaining material or small spills with inert material (dirt, sand, industrial absorbent) and then place in chemical waste containers. Flush residual spill area with large amounts of water. Dispose of all clean up materials in accordance with all applicable federal, state, and local health and environmental regulations.

Section 7: HANDLING AND STORAGE

Handling Precautions:	Sufficient ventilation should be used to maintain exposure levels below limits. If limits are exceeded a NIOSH/OSHA    	approved respirator is advisable. Chemical resistant gloves are always recommended Chemical resistant splash            	goggles are recommended when using chemicals.

Storage Requirements:	Do not store below 32Degrease F or above 100 degrease F. Do not store in direct sunlight. Keep away from heat,

Open flames or other sources of ignition. Keep away from children. Keep containers tightly closed.

Section 8: Exposure control / personal protection

EYES: 	   			Can cause severe irritation, redness, and blurred vision. Chemical resistant splash goggles are recommended

When using chemicals.

SKIN:  	  	 		Prolonged or repeated exposure can cause moderate irritation, and/or defacing of the skin. Chemical

Resistant gloves are recommended.

INHALATION: 			Headache, nasal and respiratory irritating, nausea, and drowsiness.  Local exhaust is recommended.

INGESTION:			Nausea, vomiting, and signs of nervous system depression. Do not ingest.

Exposure Guild lines:		No Available data.

Section 9: PHYSICAL AND CHEMICAL PROPERTIES

Appearance:		Yellow					Boiling Point:		 200F

Physical state:		Liquid					Freezing:		<32F

Odor:			Banana					Solubility:		Not soluble in water

pH:			8.2					Spec. Grav. / Density:	8.0

Vapor Pressure:		No data					VOC:			<15%

Section 10: STABILITY AND REACTIVITY

Stability:			Stable

Conditions to avoid:		Keep away from ignition sources, heat, sparks or flames.

Materials to avoid:		Strong acids and Oxidizers.

Hazardous Decomposition:	Carbon monoxide and other hazardous chemicals.

Hazardous Polymerization:	Will not occur.

Section 11: TOXICOLOGICAL INFORMATION

There is no data available for this product.

MATERIAL SAFETY DATA SHEET

Sunny  Wax

Section 12: ECOLOGICAL INFORMATION						Rev. Date 2/5/09		Page 2 of  3

There is no data available for this product.

Section 13: DISPOSAL CONSIDERATIONS

Dispose of in accordance with local, state, and federal regulations.

Section 14: TRANSPORT INFORMATION

Because this is produced and shipped in several different sizes as well as domestically and internationally, please consult your transportation specialist for the proper shipping name and class.

Section 15: DISCLAIMER OF LIABILITY

The information contained herein is based on data considered to be accurate. However, the information is provided without any warranty, Expressed or implied, regarding its correctness. The conditions or methods of handling, storage, use and disposal of the product are beyond Our control and may be beyond our knowledge. For this and other reasons, we do not assume responsibility and expressly disclaim liability For loss, damage or expense arising out of or in any way connected with handling, storage, use or disposal of the product.